## Slide 1: Design & Manufacture a Dual-Bladed Surgical Saw
Ibrahim Althowiqeb | 201301876
Omar Alzahrani | 201203335
Ahmad Aldakhiel | 201300056
Yazeed Almansour | 201300630
Abdullah Alotaibi | 201302697
Project Advisor: Dr. Jamal Nayfeh, Co-advisor: Dr. Panos
Team# 1
ASSE 4311: Learning Outcomes Assessment III
Senior Design Project
Derived from the United status patent did by Dr. Christopher Murphy

## Slide 2: OUTLINE
Project Introduction.
Objectives.
Project Relevance
Design Constrains.
Engineering Standards.
Conceptual Design.
Testing & Results
Conclusion & Future Recommendations
ASSE 4311: Learning Outcomes Assessment III - SDP

## Slide 3: Project Introduction
Total Joint Arthroplasty (TJA).
An oscillating saw for the resection of bones.
Dual-bladed surgical saw cuts with coincide angles.
Designing a blade assembly with a star lock adapter.
Applications:
  Dual-bladed surgical saw ready to use by the podiatrist for performing orthopedic surgeries.
  Dual-bladed surgical saw can be used to cut different locations in the human body.
ASSE 4311: Learning Outcomes Assessment III - SDP

## Slide 4: Objectives
Design a blade assembly with dual blades to cut two different planes simultaneously.
Simplifying the surgical cutting procedure by reducing sequential cuts.
Reduce surgery time.
Accurate and precise cutting action with no further need for using a cutting guide.
ASSE 4311: Learning Outcomes Assessment III - SDP

## Slide 5: Project Relevance
Orthopedic operations:
  Metatarsal bunionectomy.
  Pelvis mobilization and correction.
  Knee implant surgery.
ASSE 4311: Learning Outcomes Assessment III - SDP

## Slide 6: Design Constrains
ASSE 4311: Learning Outcomes Assessment III - SDP
CONSTRAINS
Geometrical
Ethical
Environmental & Safety
Manufacturability
Economic
Sustainability

## Slide 7: Engineering Standards
ASSE 4311: Learning Outcomes Assessment III - SDP
ASTM A36 Mild/Low Carbon Steel.
  Excellent welding properties.
  Suitable for grinding.
  Low resistance in bending.
Mechanical Properties | Metric
Tensile Strength, Ultimate | 400 - 550 MPa
Tensile Strength, Yield | 250 MPa
Elongation at Break (in 200 mm) | 20.0 %
Elongation at Break (in 50 mm) | 23.0 %
Modulus of Elasticity | 200 GPa
Bulk Modulus (typical for steel) | 140 GPa
Poissons Ratio | 0.260
Shear Modulus | 79.3 GPa

## Slide 8: Engineering Standards
ASSE 4311: Learning Outcomes Assessment III - SDP
Components | Standard | Details
Screw | ANSI metric | Torx Oval-Head Screw 3x10
Bearing | SKF | Ball bearing - Deep grove
Bearing | SKF | Needle roller bearing

## Slide 9: Conceptual Design “CAD Model”
ASSE 4311: Learning Outcomes Assessment III - SDP

## Slide 10: Conceptual Design “CAD Model”
ASSE 4311: Learning Outcomes Assessment III - SDP

## Slide 11: Conceptual Design “Equation and Parameters”
  )

## Slide 12: Conceptual Design “Configurations”
ASSE 4311: Learning Outcomes Assessment III - SDP
In line configuration.
Brushless DC motor.
Needle bearing.
Ball bearing.

## Slide 13: Testing & Results
ASSE 4311: Learning Outcomes Assessment III - SDP

## Slide 14: Testing & Results
ASSE 4311: Learning Outcomes Assessment III - SDP
Running a test on a piece of wood.
Angle of 120-degree.
Prove the concept of two blades cutting simultaneously with a precise defined angle.

## Slide 15: Conclusion and Future Recommendation
ASSE 4311: Learning Outcomes Assessment III - SDP
Replacing the motor.
Stryker seven blades.
Adding angle spacer

## Slide 16: Conclusion and Future Recommendation
ASSE 4311: Learning Outcomes Assessment III - SDP

## Slide 17
THANKS !!